Purchase Specification

for a

15" Radar Speed Sign (Solar-powered)

- Overview

Each 15" radar speed sign shall consist of a display enclosure that houses the LED boards, controller, radar, and Bluetooth hardware. Optional remote connectivity for two-way communication and control shall be available. Each 15" radar speed sign shall include a static sign mounted to the display enclosure. The 15" radar speed sign shall be pre-wired to the maximum extent possible. The 15" radar speed sign shall conform to MUTCD legibility standards for color, character, and letter height.

- Mechanical

The display enclosure and static sign shall be constructed from 0.9" (2.3mm) aluminum. All electronics shall be mounted in the display enclosure.

Display enclosure shall be a non-sealed, ventilated NEMA 3R type design. Internal components shall be easily accessible with removal of two or fewer external fasteners.

The 15" radar speed sign shall consist of modular components that are field-replaceable without complete removal of the product assembly from the mounting post or pole. The static sign, radar unit, controller board, LED display boards, and fuse(s) shall all be field-replaceable.

Display enclosure shall not exceed 26.5" (67.3cm) in length and 19.5" (49.5cm) in height. The depth of the display enclosure shall not exceed 7" (17.8cm).

Display enclosure shall be constructed to absorb impacts from thrown objects or vandalism attempts. Display window and LED boards shall deflect inwards up to 2" (5.1cm) without damaging internal components. The LEDs shall be protected by the polycarbonate window upon deflection.

Display window shall be made of ¼" (6.35mm) minimum thickness shatter-resistant UV-protected polycarbonate.

15" radar speed sign shall be designed with LED safety masking to reduce driver distractions introduced by the radar speed display. The display view shall be limited to the forward viewing angle approximately 30° from the roadside.

The display enclosure and power cabinet fasteners shall be NCHRP 350 crash test approved with the use of AASHTO or FHWA approved break-away base.

Display controller shall be reverse polarity protected.

Static sign shall adhere to MUTCD requirements of 6" increments and shall be 30" (76.2cm) wide by 42" (106.7cm) high with 15" (38.1cm) display digits. An optional 30" (76.2cm) wide by 30" (76.2cm) wide shall also be available.

Static sign letters, “YOUR SPEED” or other regulatory text, shall be printed in two lines using approximately 6" high letters. The sign background surface shall be fluorescent yellow-green, yellow, orange, or white high intensity sheeting or equivalent.

Display alignment shall be easily adjusted, without exchanging internal parts, to work on the center median, left, or right side of the roadway.

Display shall be a seven-segment design for maximum digit recognition. A full matrix or 13-segment design is not acceptable.

Each display segment shall consist of 16 discrete LEDs of approximately 15° to 17° viewing angle. LEDs shall be individually aimed to within +/- 2° of each other to concentrate light distribution within the drivers viewing area and to provide consistent cut-off of the display at the edge of the viewing cone.

Display design shall have a 1" black border around the LED sections, and shall have very high contrast between LEDs and their immediate background, to maximize visibility in direct sunlight, fog and night time conditions.

Display window shall have clear LED windows and a black surround matrix of less than or equal to 25% reflectance in accordance with the MUTCD, to maximize viewing contrast in all lighting conditions.

Display must not use anti-glare sheeting that would reduce the display’s visibility and contrast.

Non-illuminated portions of the seven segments display must not have visible “88” ghosting when a mix of on and off segments is displayed or if display is off.

Mounting:

Mounting hardware for the 15" radar speed sign shall be available for the following configurations:

- 2.5" - 3.5" OD side of pole

- 4" - 6" OD side of pole

- 6" (and greater) OD side of pole

- Flat surface

Various mounting configurations shall not require specialized tools for installation.

The 15" radar speed sign display enclosure shall be rated to a minimum of NEMA 3R.

The sign shall be 150 mph (241 km/h) wind load rated when installed as specified by the manufacturer.

The 15" radar speed sign display enclosure shall meet a system operating temperature between -40 to 167 °F (-40 to 75 °C).

Options:

15" radar speed sign shall have an optional “SLOW DOWN” message which includes LED characters approximately 6" high and shall be available in either amber or red LEDs.

Radar may optionally be externally mounted with tilt and pan adjustments for greater flexibility in alignment.

15" radar speed sign shall have optional integrated strobe(s) which shall be powered and triggered from the display’s controller at a speed threshold from 5 to 99 mph (8 to 99 km/h). Strobe may be a single white or red/blue for dual configuration.

15" radar speed sign shall support up to four optional 12" yellow LED signal modules that flash via a pre-set schedule, speed threshold, or external trigger.

The system shall include output wire harnessing for control of up to two beacons with support for up to four beacons.

The beacons shall be voltage-driven without the need for an external LED drive circuit and each beacon shall consume ≤ 5 watts when illuminated.

The LED beacons shall conform to the requirements of the Manual of Uniform Traffic Control Devices 2009 with May 2012 Revisions 1 and 2. LED beacons shall also comply with the beam shape requirements of the ITE Vehicle Traffic Control Signal Heads, Light Emitting Diode (LED) Circular Signal Supplement.

The LED beacon optics shall be premium, UV-resistant polycarbonate.

The signal housing shall meet the equipment standard of the Institute of Transportation Engineers (ITE) Vehicle Traffic Control Signal Heads (VTCSH) Chapter 2.

The signal head’s bracket assembly shall be constructed such that the signal head can be removed easily in the field.

The signal housing must be able to rotate independent from the bracket for lens alignment.

The signal housing shall be constructed from a choice of UV-resistant polycarbonate or aluminum. The signal housing shall be available in yellow, green or black.

The beacon(s) shall also be capable of being mounted to a post or pole using a separate bracket assembly to facilitate mounting multiple beacons in either vertical, horizontal, or back-to-back (bi-directional) arrangements.

The signal housing shall open for access to the wiring connections for the LED beacons. The signal housing shall be rated to NEMA 3R.

Static sign and display shall not exceed 37 lbs. (16.8 kg).

Solar Power System:

The 15" radar speed sign shall be offered with one 50-watt, 80-watt, or 170-watt 18-volt solar panel supplied with mounting hardware and bypass diode. Nominal voltage shall be 12 volts.

The solar panel shall have the capability of being mounted in a top-of-pole, or side-of-pole configuration.

The solar charge controller must provide 4-stage battery charging via pulse width modulation (PWM) and shall have the following features:

- Temperature compensation

- Low-voltage-disconnect (LVD) – to prevent complete battery discharge

- Battery, state-of-charge and battery fault LED indications

- Reverse polarity, short circuit, and over-voltage protection

The charge controller must also be impervious to water and dust ingress and have an operating temperature range from -40 to 60 °C (-40 to 140 °F).

The charge controller shall meet all requirements of Underwriters Laboratories UL 1741 and must be Class B Part 15 FCC certified.

The charge controller shall be connected to the solar panel and battery inside a weatherproof (NEMA 3R or better) enclosure in natural aluminum or light color paint to reflect sunlight for increased battery life.

Charge controller shall be field-replaceable.

Optional Integrated Solar Kit:

The 15" radar speed sign shall optionally be offered with one 30-watt or 50-watt, 18-volt, solar panel supplied with mounting hardware and bypass diodes (50-watt only). Nominal voltage shall be 12 volts.

Solar panel shall be mounted to a solar panel enclosure consisting of a formed metal enclosure that houses the charge controller and optional auxiliary batteries.

The integrated solar kit shall be capable of housing up to two 18 Ah batteries.

The integrated solar kit shall have the capability of being mounted in a top-of-pole, or side-of-pole configuration.

The integrated solar kit incorporate a 45-degree cast mount with an industry standard 1.5 NPSM thread for use with top-of-pole adapters, or any other hardware or fittings that use the same thread.

The solar charge controller must provide 4-stage battery charging via pulse width modulation (PWM) and shall have the following features:

- Temperature compensation

- Battery, state-of-charge, and battery fault LED indications

- Reverse polarity, short circuit, and over-voltage protection

The charge controller must also be impervious to water and dust ingress and have an operating temperature range from -40 to 60 °C (-40 to 140 °F).

Charge controller shall be field-replaceable.

The charge controller shall meet all requirements of Underwriters Laboratories UL 1741 and must be Class B Part 15 FCC certified.

The charge controller shall be connected to the solar panel and batteries inside a weatherproof (NEMA 3R or better) enclosure in natural aluminum to reflect sunlight for increased battery life.

- Electrical

Radar device shall meet specifications for an FCC part 15 Low Power Device - 24.150 GHz (K-band) and shall not require an operating license.

The radar shall have a reporting accuracy of +/- 1 mph and shall be set to detect approaching vehicles only.

The 15" radar speed sign shall have a detection range for oncoming vehicles of: 5 to 99 mph (8 to 99 km/h).

Radar shall operate on voltages from 10.5VDC to 16.8VDC and shall consume less than 1/3 amp at 12VDC, typically <1/10 amp.

The 15" radar speed sign shall be capable of displaying the numeric readout value within one second of detection of a vehicle and shall hold the detected speed for approximately one second after the vehicle passes outside the detection area and return to standby mode with a blank display when no vehicles are present.

The 15" radar speed sign, with the LEDs illuminated at full intensity, shall consume less than 6.5 watts maximum of DC power; with a typical power requirement of 3.5 watts and shall consume less than 1.75 watts in stealth mode (collecting data but no display); shall consume less than 0.95 watts in standby.

The system shall use an ambient brightness sensor for automatic nighttime dimming.

Battery System:

The battery cabinet shall house one 35 Ah, 55 Ah or 100 Ah sealed 12-volt valve-regulated AGM lead-acid maintenance-free battery. The battery shall be equipped with a fast-acting 15-amp cartridge fuse on the positive lead.

The battery, in conjunction with recommended 15" radar speed sign performance, shall be designed for a demonstrable service life of up to 5 years.

The operating temperature range of the battery shall be -40 to 140 °F (-40 to 60 °C).

Battery shall be readily available from multiple suppliers and non-proprietary. Battery shall be field-replaceable.

Battery shall be supported from the sides and from the rear by rubber bumpers.

- Solar Simulations (If Applicable)

Detailed solar simulations shall be provided as evidence that the 15" radar speed sign is capable of meeting the performance requirements at a specific location. Solar Simulations shall clearly demonstrate these key performance indicators: Energy-In, Energy-Out, Array-to-Load Ratio (ALR), and Autonomy. The manufacturer or bidder shall provide a detailed analysis of these calculations in a “Solar Power Report.”

Monthly average sunlight (insolation), night length and temperature data for a specific, declared location shall be from recognized public sources such as the NASA Atmospheric Sciences Data Center. All sources shall be cited exactly and accessible online without cost to allow verification of the data.

Energy Balance:

During a normal 24-hour cycle of operation, a solar-powered 15" radar speed sign will take energy in from the sun and consume energy through the flashing of the display, general quiescent power draw and optional strobes, beacons or other devices. Energy Balance refers to the evaluation of these energy values to determine overall system sustainability and resistance to variances in sunlight and activation load.

Energy Balance compares Energy-In and Energy-Out. Calculations shall be performed for the “Worst Month” of the year where worst month is determined by the lowest value of Energy-In divided by Energy-Out.

Energy-In:

Energy-In is the total amount of sunlight energy in watt-hours available to the 15" radar speed sign over a 24-hour period. Energy-In is available to operate the 15" radar speed sign, charge the battery, or both. Energy-In shall be determined as follows:

- Insolation X Panel Wattage X Shading X charging efficiency X Battery charge acceptance

- The energy from the solar panel shall be based on available solar radiation at the installation location for the panel’s inclination angle. The solar radiation (insolation) values used shall be for the worst-case month of the calendar year.

- Shading from nearby trees, buildings or other structures unique to a particular location are to be factored-in and the calculations shall clearly show and justify the de-rating of the solar panel energy input. A photograph showing the sun’s path and obstructions it encounters shall be included.

Energy-Out:

Energy-Out is the total amount of energy in watt-hours consumed by the 15" radar speed sign in a 24-hour period of normal operation.

Energy-Out is the sum of quiescent and operating loads, measured in watt-hours, in all circuitry over 24 hours, including:

- Solar charge controller quiescent draw

- Radar “detection mode” and idle quiescent draw

- System controller quiescent draw when no vehicles are being detected

- System “active” load when vehicles are being detected and display is active – in both day and night modes.

- The simulations shall clearly detail both the number of sign display activations due to vehicle volume and any third-party device load variations based on scheduling.

ALR (Array-to-Load Ratio):

System Array-to-Load (ALR) ratio shall be calculated as:

- Daily Available Energy-In divided by Daily Energy-Out as defined above

15" radar speed sign solar simulations shall be calculated demonstrating a minimum Array-to-Load (ALR) ratio of 1.2:1 (1.2).

Autonomy:

Autonomy is the number of days that the 15" radar speed sign can continue to operate normally in the absence of any solar charging. Autonomy shall be calculated as follows:

- (Nominal Battery Capacity de-rated for Temperature minus battery capacity unavailable due to Low Voltage Disconnect) divided by (Daily total energy consumption at specified ADT or as otherwise specified).

15" radar speed sign autonomy shall be a minimum of 7 days.

- Configuration and Operation

The 15" radar speed sign programming software and mobile app shall maintain settings and schedules indefinitely.

Display shall have the following speed threshold programming capabilities:

- Display on/off (stealth mode)

- Minimum displayed speed

- Speed limit

- Flashing digits in excess of pre-set violation threshold

- High-speed blank-out threshold

Display digits shall flash upon breach of the violation threshold at a user selectable rate from 30 – 150 FPM, factory programmed to 109 FPM.

The radar sign shall have integrated data collection and scheduling capabilities. Data collection function shall have the capacity to record over 300,000 individual data points which include date, time, and speed.

Scheduling shall be able to be programmed and uploaded to the 15" radar speed sign from a compatible mobile device.

Vehicle data from the 15" radar speed sign shall be able to be downloaded from a compatible mobile device and distributed via SMS or email.

Vehicle data shall be formatted as a .csv file that can be imported into other traffic analysis tools.

Optional traffic analysis software shall be available. The software shall have the ability to analyze traffic data that has been downloaded from the sign. The software shall have the ability to display  the date, speed and time of the vehicle, the number of daily vehicles, average daily volume, posted speed, average speed, vehicles within user-specified percentiles (typically 50th and 85th percentiles), and percent compliance. The software shall also contain filters for creating customized reports.

The 15" radar speed sign mobile app shall allow programming, scheduling, data downloads, and diagnostics to be accessible via Bluetooth wireless link to a Windows-compatible computer or mobile device, and shall have the following display diagnostics:

- Test the real-time connection to the sign

- Run a test sequence that initiates a display digit roll-up test to verify the sign is operating properly

- System voltage check, to confirm the battery voltage

- Validate real-time vehicle count to determine if data is being collected and radar is operational

- Ability to verify and update to new firmware versions

- Program and upload schedules

The 15" radar speed sign shall be capable of displaying numbers from 1 to 99 with display in mph or km/h as selected.

The display shall have the option to trigger up to two external 12V devices at different speed thresholds or be controlled by time of day to support integration of external flashers or other devices.

The mobile app shall be available free of charge on the Apple App Store or Google Play Store for compatible devices. The mobile app can be used in conjunction with the Windows-based software and shall mimic the functionality to the maximum extent possible.

The 15" radar speed sign shall have the capability to integrate with third-party hardware and web-based applications for remote settings control, scheduling, monitoring of system voltage, detected speeds, communication events, and errors.

Optional ethernet connectivity shall be available for remote programming, scheduling, diagnostics, and traffic data.

Optional “SLOW DOWN” message shall display at a preset speed threshold. The display shall alternate between the driver’s speed and “SLOW DOWN” until the high-speed blanking threshold is met, and then only “SLOW DOWN” is displayed.

- Remote Monitoring (Optional)

The 15" radar speed sign shall have the optional capability to remotely connect to a cloud-based platform allowing for two-way communication and control. The monitoring unit shall be mounted in the control cabinet and include a GPS and cellular modem with optional ethernet connection and RS-232 port.

Monitoring Unit:

The monitoring unit shall be a single piece of equipment housed within the control cabinet and shall not require any peripheral attachments except for the GSM and GPS antenna lead wires for the externally mounted antenna.

The externally mounted integrated GSM/GPS antenna shall be a suitable weather-resistant design and shall mount directly to the top surface of the control cabinet without the requirement for additional hardware.

The monitoring unit shall be capable of being programmed locally via a laptop interface and ethernet.

The monitoring unit shall be capable of receiving over-the-air software and security updates via cellular communication. Physical trips to the monitoring unit shall not be required for updates.

The monitoring unit shall be connected-vehicle ready and capable of communicating safety messages to motorists via cellular infrastructure and a mobile application. The monitoring unit shall support the SAE J2735 standard for connected vehicle messages. The monitoring unit shall support both cellular and optional DSRC technology. The mobile application is freely available to all users, including pedestrians, cyclists, and motorists.

Connectivity and Support Plan:

The 15" radar speed sign shall include cloud-hosted software with user web-based access.

The user interface shall be web-based and viewable using any modern web browser such as Chrome, Edge, Firefox, or Safari. This compatibility extends to mobile devices that are able to access fully featured web browsers.

Cellular communication shall use the latest 4G LTE wireless broadband networks.

1/2/3/4/5-year connectivity and support plans shall be available.

The cloud software shall be mobile friendly and operate without requiring a static IP address. Operators shall be able to access the data and control the 15" radar speed sign via a mobile device.

Over-the-air software and security updates shall be available, and hardware shall be upgradeable if the service provider changes network requirements.

The user interface shall include a scrollable, zoomable map display, with the 15" radar speed sign shown as a representative dynamic icon on the map. The map display must have the option of satellite view or standard street view. The map shall include the ability to see the 15" radar speed sign icons using Google Street View.

The icons shall be able to identify if there is an alert status or if the 15" radar speed sign is offline.

The map display shall allow the operator to turn on layers which can display all 15" radar speed sign designations. Operators shall also be able to Google traffic overlay information so they can see traffic together with the 15" radar speed signs.

An integrated GPS shall provide 15" radar speed signs geolocation.

If cell service is interrupted or unavailable, events shall be stored in internal memory, and automatically forwarded when cell service is restored. Battery back-up shall also be available for continual operation.

The monitoring unit shall autonomously ping the cellular network every 15 minutes to ensure online connectivity.

HTTP and HTTPS protocols and XML data structures for communications shall be utilized.

The cloud software shall meet NEMA TS 8 requirements for Cyber and Physical Security for Intelligent Transportation Systems.

The user interface shall display the alert/fault status, last communication with the device, real-time, minimum, and maximum values for battery voltage, and on/off status. These parameters can be viewed in graphical form.

When a fault occurs, real-time alerts shall be published via SMS and/or email. The alert will be immediately sent to the response personnel.

Key performance indicators shall be recorded by the software and reported on a weekly or daily basis. The report shall include details on the health condition of the battery. The following types of reports shall be available: Alerts, User-Activity, Operation, and Fault Repair Response Time.

Alerts shall be displayed by color codes to indicate priority and critical nature of the alert.

Raw data, error logs, and communication logs shall be available for diagnostics. The logs shall be print-ready or downloadable to spreadsheet.

Speed thresholds, schedules, or program delays shall be set-up and downloaded remotely from the cloud-based storage via the web-based user interface. The schedule shall be published to one or more 15" radar speed signs simultaneously.

Real time graphs of vehicle speeds and volumes shall be viewable including the median speed, 85th, and 95th percentiles, and volume of vehicles per hour - based on 15-minute interval, average values.

The user interface shall have the following programmable options: sign mode (on/off), speed offset, speed limit, minimum display speed, violation alert flashing speed, and maximum display speed. Stealth mode for data collection shall also be programmable.

- Optional Configuration

The 15" radar speed sign may be configured with any of the following options:

- Integrated solar kit (see Section 2.0)

- “SLOW DOWN” message (see Section 2.0)

- Externally mounted radar (see Section 2.0)

- Integrated strobes (see Section 2.0)

- Up to four circular beacons (see Section 2.0)

- Ethernet connectivity (see Section 5.0)

- Cellular connectivity (see Section 6.0)

- Qualifications

The 15" radar speed sign shall be FCC certified to comply with all 47 CFR FCC Part 15 Subpart B Emission requirements.

The 15" radar speed sign shall be manufactured in the USA and shall be Buy America compliant.

Manufacturer shall provide a 3-Year Limited Warranty.

The Manufacturer shall be ISO 9001 certified.

The unit shall be manufactured by Carmanah Technologies.

Manufacturer: Carmanah Technologies Inc.

Model: SPEEDCHECK-15 radar speed sign

Toll-Free: 1-877-722-8877

www.carmanah.com

*Battery warranty shall be covered by a 1-Year Limited Warranty.

*Optional cellular remote connectivity shall increase the battery warranty to match the connectivity plan (ie. either 1/2/3/4/5-years), or as long as the plan is.