Purchase Specification

for a

Solar Self-Contained School Zone Beacon (SZB) with Remote Connectivity

- Overview

Each SZB shall have the capability to remotely connect to a cloud-based monitoring platform allowing for two-way communication and control. Each SZB system shall consist of a self-contained solar engine that houses the charge controller, flash controller, on-board user interface, optional wireless communications, batteries, solar panel and a monitoring unit which includes GPS and cellular modem with optional ethernet connection and RS-232 port.  Each SZB system shall include either one, two or three 8” or 12” LED modules and signal housings separately mounted or integrated with the solar engine. The SZB shall be pre-wired to the maximum extent possible. The SZB shall conform to all applicable provisions of the MUTCD Chapter 4L, including flash pattern. The system shall also have the capability of meeting the ITE intensity requirement for vehicle traffic signals.

- Mechanical Specifications

The solar engine shall be constructed from aluminum with an integrated solar panel.  All batteries, electronics, monitoring unit and cellular modem shall be mounted in the solar engine, with no external control cabinet or battery cabinet required.

The solar engine, excluding mounting components, shall not exceed 22” in width, 16” in height, and 5” in depth.

The overall weight of the solar engine assembly (including two batteries but not including lightbars or pushbutton) shall not exceed 40 lbs. (18.2 kg).

The solar engine shall be supplied with a fixed tilt angle of 45 degrees and shall be able to be oriented toward the equator with no additional mounting hardware.

Access to the interior of the solar engine shall be provided by a lid that is hinged on the bottom edge and is fitted with a foam gasket.  The lid shall have a lockable latch.

The solar engine shall be vented to provide cooling of the battery and electronic system.  The vents shall be screened to prevent ingress by insects and debris.

Fasteners shall be stainless steel.

The internally mounted monitoring unit shall be a single piece of equipment and not require any peripheral attachments except for the GSM and GPS antenna lead wires for the externally mounted antenna.

The externally mounted integrated GSM/GPS antenna shall be a suitable weather-resistant design and shall mount directly to the top surface of the control cabinet without the requirement for additional hardware.

The monitoring unit shall be capable of being programmed locally via a laptop interface and ethernet.

The monitoring unit shall be capable of receiving over-the-air software and security updates via cellular communication. Physical trips to the monitoring unit shall not be required for updates.

The monitoring unit shall be connected-vehicle ready and capable of communicating safety messages to motorists via cellular infrastructure and a smartphone app. The monitoring unit shall support the SAE J2735 standard for connected vehicle messages. The monitoring unit shall support both cellular and optional DSRC technology. The smartphone app shall be freely available to all users, including pedestrians, cyclists and motorists.

Schedules shall be locally saved in the monitoring unit.  The monitoring unit shall be able to update its internal time clock from the server and/or GPS to ensure clock accuracy within one minute of actual time.

The monitoring unit shall be covered under warranty if the device is under an active connectivity and support plan and is connected to the SZB.

- Fixtures

- Circular Beacons

The LED beacons shall conform to the requirements of the Manual of Uniform Traffic Control Devices 2009 with May 2012 Revisions 1 and 2. LED beacons shall also comply with the intensity and beam shape requirements of the ITE Vehicle Traffic Control Signal Heads, Light Emitting Diode (LED) Circular Signal Supplement.

The SZB shall be capable of driving beacons at ITE-compliant intensities if solar conditions and programming configuration permit it.

The beacons shall be current-driven LED strings without active electronics.  The LEDs shall be driven by pulse-width modulated fixed current.

The LED beacons shall be available in red and yellow, and in 12” (305mm) and 8” (203mm) diameters.

The LED beacon optics shall be premium, UV-resistant polycarbonate.

LED Beacon wiring harnesses shall be included.

- LED Enhanced Signs

The SZB shall be able to optionally operate flashing LEDs in the border of a sign.

- Signal Housing

The solar engine shall be capable of direct attachment to the top of a signal head.  The signal head shall contain mechanical reinforcement designed specifically to support the weight of the solar engine.

The signal housing shall meet the equipment standard of the Institute of Transportation Engineers (ITE) Vehicle Traffic Control Signal Heads (VTCSH) Chapter 2.

The signal head’s bracket assembly shall be constructed such that the signal head can be removed easily in the field.

The signal housing must be able to rotate independently from the solar engine or bracket for lens alignment.

The signal housing shall be constructed from either UV-resistant polycarbonate or aluminum.  The signal housing shall be available in yellow, green or black.

The beacon(s) shall also be capable of being mounted to a post or pole using a separate bracket assembly to facilitate mounting multiple beacons in either vertical, horizontal, or back-to-back (bi-directional) arrangements.

The signal housing shall open for access to the wiring connections for the LED beacons. The signal housing shall be rated to NEMA 3R.

- Mounting

Solar engine mounting adapter hardware for the SZB and LED Enhanced sign shall be available for the following configurations:

Direct to top of signal housing

2” / 2.5” Perforated Square Pole Mount

2 3/8” - 2 7/8” Diameter Round Post Mount

4” - 4.5” Diameter Round Post Mount

Side-of-Pole Mount

Wooden Pole

Signal housing shall be able to mount in a single or dual (vertical, horizontal or back-to-back) configuration.  LED-enhanced signs shall be able to mount in a single or back-to-back (bi-directional) configuration.

Mounting configurations shall not require specialized tools for installation.

- Connectivity and Support Plan

The SZB shall include cloud hosted software with user web-based access.  Other software or IT infrastructure shall not be required for installation or maintenance.

The software shall be viewable using a browser, either: Chrome, Internet Explorer, or Firefox, as well as Safari on an iPad.

Cellular communication shall use the latest 3G, 4G and LTE wireless broadband networks.

The software shall be smartphone friendly and operate without requiring a static IP address.  Operators shall be able to access the data and control the SZB via a smartphone phone.

Over-the-air software and security updates shall be available; hardware upgrades are included in the plan. If the service provider changes network requirements, the connectivity and support plan include all software and hardware upgrades.

An integrated GPS shall allow SZB geolocation.

If cell service is interrupted or unavailable, events shall be stored in internal memory, and automatically forwarded when cell service is restored.  Battery back-up shall also be available for continual operation.

The monitoring unit shall ping the cellular network every 30 minutes to ensure online connectivity.

1/2/3/4/5-year connectivity and support plans shall be available.

- Software User Interface

The software user interface shall include a scrollable, zoom-able map display, with the SZB shown as a representative dynamic icon on the map. The map display must have the option of satellite view or standard street view. The map shall include the ability to see the SZB icons using Google Streetview.

The icons shall be able to identify if there is an alert status or if the SZB is offline.

The map display shall allow the operator to turn on layers which can display all SZB designations.  Operators shall also be able to overlay Google traffic information so they can see traffic together with the SZBs.

HTTP and HTTPS protocols and XML data structures for communications shall be utilized.

The software is cloud-based and shall meet NEMA TS 8 requirements for Cyber and Physical Security for Intelligent Transportation Systems.

The software shall display the alert/fault status, last communication with the device, real-time, minimum and maximum values for battery voltage, solar panel voltage, on/off status, door open/closed, or local manual override control. These parameters can be viewed in graphical form.

When a fault occurs, real-time alerts shall be published via SMS and/or email.  The alert will be immediately sent to the response personnel.

Key performance indicators shall be recorded by the software and reported on a weekly or daily basis. The report shall include details on the health condition of the batteries, solar panels and LED modules. The following types of reports shall be available: Alerts, User-Activity, SZB Operation, Fault Repair Response Time.

Alerts shall be displayed by color codes to indicate priority and critical nature of the alert.

Raw data, error logs, and communication logs shall be available for diagnostics.  The logs shall be print-ready or downloadable to spreadsheet.

SZB schedules, events, holidays, and program delays shall be set-up and downloaded remotely via the software.  The schedule shall be published to one or more SZBs simultaneously.

The software shall be capable of immediate manual override of individual or networks of SZBs in the event of early release or other unexpected school events.

Up to 20 unique schedules, unlimited holidays, exceptions, and overrides shall be available.

- Smartphone Mobile Safety App

The smartphone app shall be compatible with iOS and Android devices.

The smartphone application shall provide audible alerts to users. The application shall not require any user interaction and shall always run in the background.

Users shall be capable of receiving visual alerts via the smartphone application.

Users shall be capable of seeing speed limits for active school zones and receive warnings when speeding in an active school zone.

Users shall have the ability to turn on/off audible alarms for the various applications.

Users shall be capable selecting the form of transportation, such as pedestrian, cyclist, or motorist.

The smartphone application shall support the following applications as standard:

- SPaT/MAP display of signal timing – V2I

- Red-light running at traffic signals – V2I

- Emergency vehicle and bus priority – V2I

- Direction of approaching emergency vehicle – V2V

- Intelligent cross walks – V2I

- Intelligent school beacons – V2I

- Motorist to Cyclist and Pedestrians Warnings - V2V

- Rear end collision warning – V2V

- Virtual/advance traffic detectors at traffic signals – V2I

- Curve warning/reduce speed – V2I

- Wrong way detection – V2I

- Configuration

The SZB enclosure shall house an auto-scrolling LED on-board user interface that provides on-site configuration adjustment, system status and fault notification, built-in system test, and programming of optional internal calendar settings. The SZB shall have an optional USB interface for programming the internal calendar, and an optional pole-mounted programming junction box for housing the USB interface.

The user interface shall provide a display of four (4) alphanumeric characters and three (3) control buttons to navigate and change settings and activate functions.

When editing the configuration, the user interface will flash the display indicating it is ready to accept editing and will flash the display rapidly 3 times to indicate the setting change has been accepted.

The system shall provide configurable nighttime intensity settings ranging from 10% to 100% of daytime intensity.

The SZB shall be provided with an optional built-in internal calendar function that allows users to program multiple on/off sequences every day for at least one calendar year.  The calendar shall be programmed via USB connection made available to users within the solar engine.  An optional external weather-proof box and harnessing shall be made available for programming of the SZB from the base of the mounting structure.

The beacons will flash when activated either by an optional internal calendar within the controller or by contact closure provided by a third-party device.  Flashing will continue until either the internal calendar discontinues it or contact closure from the monitoring unit or a third-party device is removed.  Contact closure control by third-party devices shall be offered as “Normally Open” or “Normally Closed”.

The system shall be capable of enabling or disabling ambient brightness auto-adjustment.  This feature allows the system to provide optimal output brightness in relation to ambient light levels. If enabled, the ambient brightness auto-adjustment shall adjust output to a range between 50% and 100% of daytime intensity.

The User Interface shall provide viewing and/or programming access for the following:

- Digital output that is active during the flashing cycle that allows the notification or control of external devices such as overhead illumination.  Digital output shall be configurable for night operation only or operation day or night

- 6 Flash Patterns

- Radio Channel (Choice of 1 to 14) if equipped

- Radio Status if equipped

- Calendar On/Off Control

- Calendar Master/Slave control of calendar broadcast via radio if equipped

- Night Intensity Setting

- Adjustment for Ambient Daytime Brightness

- Intensity (20 mA to 1400 mA)

- Self-Test / BIST (Built-In Self-Test) including the detection of shorts or open circuits in the fixture outputs

- Battery Status – General description and actual battery voltage

- Day or Night Status (as determined by dedicated photosensor not solar panel output)

- Solar Panel Voltage

- Automatic Light Control.  If this safety feature is enabled, it allows the SZB to temporarily reduce the intensity of the beacons to maintain energy equilibrium. The user interface shall report the amount of dimming being applied in the range of 10% to 100%

- Firmware Version number

On/off activation, night intensity setting and adjustment for ambient daytime brightness shall be automatically broadcast to all radio-equipped SZBs in the system when changed in one radio-equipped SZB.

- Solar Panel System

The solar engine shall include one 18V nominal solar panel rated at 30 watts with bypass diode.  The solar panel shall be no larger than the footprint of the solar engine enclosure.

Electrical connections on the back of the solar panel shall be contained with an enclosure that prevents accidental contact with either of the power leads.

The solar charging system shall use maximum power point tracking (MPPT).

- Battery System

The solar engine shall house two 18 amp-hour 12V nominal sealed valve-regulated AGM lead-acid maintenance-free batteries.  Each battery shall be equipped with a minimum 1.5-amp fuse on the positive lead.

The battery charging system shall be 3-stage and incorporate temperature-compensation to prevent battery overcharging in hot weather.

Batteries, in conjunction with recommended RRFB performance, shall be designed for a demonstrable service life of 5 years.

The battery shall be rated for -40˚ to 140˚F (-40˚ to 60˚C).

Batteries shall have quick connections to facilitate installation and be readily available from multiple suppliers and non-proprietary.

Batteries shall be supported by rubber bumpers and constrained from excessive movement.

- Operational Specifications

The SZB shall conform to all applicable provisions of the MUTCD and shall provide configurable intensity settings up to and including the ITE VTCSH LED circular signal supplement requirement.

The SZB shall offer an MUTCD-compliant flash pattern and activation including alternate, unison and quick-flash

The SZB shall conform to the provisions of the MUTCD 2009 Edition Chapter 4L. Flashing Beacons standard of a flash rate of not less than 50 or more than 60 times per minute, where the illuminated period of each flash shall be a minimum of 1/2 and a maximum of 2/3 of the total cycle.

The SZB shall use a dedicated light sensor to detect night and day states and apply any optionally-enabled intensity adjustments.

The SZB, including the approved third-party time switch, shall have the capacity to operate at an agency-specified number of hours per day, and a specified number of days per week using the available solar radiation at the installation location.

- Radio System

The SZB shall have an optional 2.4GHz radio that allows one “Master” SZB equipped with internal or external calendar system to remotely command multiple “Slave” SZBs within range to turn ON or OFF in synchrony with the Master SZB.

The SZB shall have the capability to activate other SZBs by wireless communications within 1,000 feet (304 meters).

The SZB shall have a minimum of 14 unique channels that can be configured on-site to avoid inadvertent activation of nearby systems.

The antenna shall be a low-profile “button” shape that cannot be bent or broken by vandals

All SZBs in the system shall initiate activation simultaneously within 150ms of activation.

- Activations

The SZB shall be activated remotely by the factory-installed monitoring unit or activated locally via included operational mode switch.

With optional local wireless, all SZBs in a master/slave configuration shall initiate activation simultaneously within 150ms of activation.

- Solar Simulations

Detailed solar simulations shall be provided as evidence that the SZB is capable of the claimed performance at a specific location.  Solar Simulations shall be composed of three calculations: Energy Balance, Array-to-Load Ratio (ALR), and Autonomy.  The manufacturer or bidder shall provide a detailed analysis of these three calculations in an “Energy Balance Report”.

Monthly average sunlight (insolation), night length and temperature data for a specific, declared location shall be from recognized public sources such as the NASA Atmospheric Sciences Data Center.  All sources shall be cited exactly and accessible online without cost to allow verification of the data.

Energy Balance

During a normal 24-hour cycle of operation, a SZB will take energy in from the sun and consume energy through the flashing of the beacons, radio communication (if equipped), and general quiescent power draw.  Energy Balance refers to the evaluation of these energy values to determine overall system sustainability and resistance to variances in sunlight and activation load.

Energy Balance compares Energy-In and Energy-Out. Calculations shall be performed for the “Worst Month” of the year where worst month is determined by the lowest value of Energy-In divided by Energy-Out.

Energy-In

Energy-In is the total amount of sunlight energy in watt-hours available to the SZB over a 24-hour period.  Energy-In is available to operate the SZB, charge the battery, or both. Energy-In shall be determined as follows:

Insolation X Panel Wattage X Shading X charging efficiency X Battery charge acceptance

- The energy from the solar panel shall be based on available solar radiation at the installation location for the panel’s inclination angle.  The solar radiation (insolation) values used shall be for the worst-case month of the calendar year.

- Shading from nearby trees, buildings, or other structures unique to a particular location are to be factored-in and the calculations shall clearly show and justify the de-rating of the solar panel energy input.  A photograph showing the sun’s path and obstructions it encounters shall be included.

- Batteries shall be returned to full charge by sunset at the end of each day.

Energy-Out

Energy-Out is the total amount of energy in watt-hours consumed by the SZB in a 24-hour period of normal operation.

Energy-Out is the sum of quiescent and operating loads, measured in watt-hours, in all circuitry over 24 hours with an operating capacity of 600 20-second activations, including:

- Controller quiescent draw (daytime and between flashes)

- Wireless quiescent draw (if equipped) calculated over 24 hours.

- Operating load of LED beacons including pedestrian indicators at rated intensity per activation.  The number of LED beacons and their electrical load details (voltage, current and power when lit) shall be clearly indicated;

- Energy adjustments due to LED drive circuit efficiency.

- The simulations shall clearly detail the flash pattern being used and calculate the duty cycle of the pattern.

- Calculations shall assume the 90% of flashing occurs during daytime.

ALR (Array-to-Load Ratio)

System Array-to-Load (ALR) ratio shall be calculated as: Daily Available Energy-In divided by Daily Energy-Out as defined above.

SZB Solar Simulations shall be calculated demonstrating a minimum Array-to-Load (ALR) ratio of 1.2:1 (1.2)

Autonomy

Autonomy is the number of days that the SZB can continue to operate normally in the absence of any solar charging.  Autonomy shall be calculated as follows:

(Nominal Battery Capacity de-rated for Temperature minus battery capacity unavailable due to Low Voltage Disconnect) divided by (Daily total energy consumption for the specified total hours of operation)

SZB autonomy shall be a minimum of 5 days.

- Environmental Testing

The SZB cabinet and LED beacons shall be rated to a minimum of NEMA 3R.

- Packaging

Packaging shall consist of only recyclable corrugated cardboard and soft plastic bags.

- Qualifications

The SZB shall be FCC certified to comply with all 47 CFR FCC Part 15 Subpart B Emission requirements.

The SZB shall be manufactured in the USA and shall be Buy America compliant.

Manufacturer shall provide a 5-Year Limited Warranty.  Battery warranty shall match the connectivity plan (ie. either 1/2/3/4/5-years).

The Manufacturer shall be ISO 9001 certified.

The SZB shall be manufactured by Carmanah Technologies Inc.

Manufacturer: Carmanah Technologies Inc.

Model: R829-F Solar Crosswalk Flashing Beacon with StreetHub

Toll-Free: 1-877-722-8877

www.carmanah.com