Purchase Specification

for a

AC-Powered Cabinet-Based School Zone Beacon (SZB) with Remote Connectivity

- Overview

Each SZB shall have the capability to remotely connect to a cloud-based platform allowing for two-way communication and control.  Each SZB shall be cabinet-based and use AC power with circular beacons mounted separately.  The industry-standard cabinet will house the charge controller, flash controller, on-board user interface, optional wireless communications, AC/DC power supply, circuit breakers and a monitoring unit which includes GPS and cellular modem with optional ethernet connection and RS-232 port. Each SZB shall include one, two, three or four 8” or 12” LED modules and signal housings.  The SZB shall be pre-wired to the maximum extent possible. The SZB shall conform to all applicable provisions of the MUTCD Chapter 4L, including flash pattern. The system shall also have the capability of meeting the ITE intensity requirements for vehicle traffic signals.

- Mechanical Specifications

The control cabinet shall be constructed from aluminum with a industry standard #2 lock and tamper-proof hinged door.  No other external control cabinet shall be required. The control cabinet shall be vented to provide air circulation and cooling of the electronic system.  The vents shall be screened to prevent ingress by insects and debris. Interior space and mounting methods shall be provided for third-party time switches such as RTC and Applied Information.

The overall weight of the control cabinet shall not exceed 90lbs (41 kg) and shall have the approximate dimensions: 24” H x 16” W x 8” D (61cm H x 41cm W x 21 cm D).

Fasteners shall be stainless steel.

The internally mounted monitoring unit shall be a single piece of equipment and not required any peripheral attachments except for the GSM and GPS antenna lead wires for the externally mounted antenna.

The externally mounted integrated GSM/GPS antenna shall be a suitable weather-resistant design and shall mount directly to the top surface of the control cabinet without the requirement for additional hardware.

The monitoring unit shall be capable of being programmed locally via a laptop interface and ethernet.

The monitoring unit shall be capable of receiving over-the-air software and security updates via cellular communication. Physical trips to the monitoring unit shall not be required for updates.

The monitoring unit shall be connected-vehicle ready and capable of communicating safety messages to motorists via cellular infrastructure and a smartphone app. The monitoring unit shall support the SAE J2735 standard for connected vehicle messages. The monitoring unit shall support both cellular and optional DSRC technology. The smartphone app shall be freely available to all users, including pedestrians, cyclists and motorists.

Schedules shall be locally saved in the monitoring unit.  The monitoring unit shall be able to update its internal time clock from the server and/or GPS to ensure clock accuracy within one minute of actual time.

The monitoring unit shall be covered under warranty if the device is under an active connectivity and support plan and is connected to the SZB.

- Fixtures

- Circular Beacons

The LED beacons shall conform to the requirements of the Manual of Uniform Traffic Control Devices 2009 with May 2012 Revisions 1 and 2. LED beacons shall also comply with the intensity and beam shape requirements of the ITE Vehicle Traffic Control Signal Heads, Light Emitting Diode (LED) Circular Signal Supplement.

The SZB shall be capable of driving beacons at ITE-compliant intensities.

The beacons shall be current-driven LED strings without active electronics.  The LEDs shall be driven by pulse-width modulated fixed current.

The SZB shall support one, two, three, or four LED beacons.  The SZB shall support 12” (305mm) and 8” (203mm) LED signal modules.  The LED signal modules must be yellow.

The LED beacon optics shall be premium, UV-resistant polycarbonate.

LED Beacon wiring harnesses shall be included.

- LED Enhanced Signs

The LED enhanced sign shall be available in 24, 30, 36, or 48” and typical MUTCD crossing warning signs such as the W11-2 (Pedestrian), W11-15 (Trail) and S1-1 (School) as applicable in MUTCD Chapter 2C and Chapter 7B respectively.  The sign sheeting shall be yellow or fluorescent yellow green (FYG) 3M Diamond Grade DG3 retroreflective with 3M anti-graffiti and overlay film or High Intensity Prismatic sheeting.

The LED enhanced sign shall consist of 8 yellow high-power LEDs in waterproof, polycarbonate impact-resistant housings that can be driven at a high intensity. Each housing shall be IP68 rated and tested for shock and vibration.

The LED optics shall be integrated total internal reflection (TIR) for optimal light efficiency and shall be premium, UV-resistant polycarbonate.  The optics shall be purpose-built by the manufacturer for optimal intensity.

In the event a single LED fails, all other LEDs shall continue to operate.

The LEDs shall be current-driven strings without active electronics.  The LEDs shall be driven by pulse-width modulated fixed current.

The LED bezel shall be black and placed within the border of the sign for enhanced LED contrast and increased visibility.

The LED wiring shall be covered by aluminum channels. There shall be no gaps or exposed wiring between the channels and LED modules or from the sign to the pole. All harnessing must be concealed and vandal resistant.

- Signal Housing

The signal housing shall meet the equipment standard of the Institute of Transportation Engineers (ITE) Vehicle Traffic Control Signal Heads (VTCSH) Chapter 2.

The signal head’s bracket assembly shall be constructed such that the signal head can be removed easily in the field.

The signal housing must be able to rotate independently from the solar engine or bracket for lens alignment.

The signal housing shall be constructed from either UV-resistant polycarbonate or aluminum.  The signal housing shall be available in yellow, green or black.

The beacon(s) shall also be capable of being mounted to a post or pole using a separate bracket assembly to facilitate mounting multiple beacons in either vertical, horizontal, or back-to-back (bi-directional) arrangements.

The signal housing shall open for access to the wiring connections for the LED beacons.  The signal housing shall be rated to NEMA 3R.

- Mounting

Mounting adapter hardware for the SZB cabinet shall be available for 4” – 4.5” (101mm – 114mm) round poles or square posts.

Side-of-Pole mounting shall offer banding, Z-bar or U-bolt mounting as standard. Signal housing shall be able to mount in a single or dual (vertical, horizontal or back-to-back) configuration.  LED-enhanced signs shall be able to mount in a single or back-to-back (bi-directional) configuration.

Mounting configurations shall not require specialized tools for installation.

- Connectivity and Support Plan

The SZB shall include cloud hosted software with user web-based access.  Other software or IT infrastructure shall not be required for installation or maintenance.

The user interface shall be web based and viewable using a browser, either Chrome, Internet Explorer, or Firefox, as well as Safari on an iPad.

Cellular communication shall use the latest 3G, 4G and LTE wireless broadband networks.

The cloud software shall be smartphone friendly and operate without requiring a static IP address.  Operators shall be able to access the data and control the SZB via a smartphone phone.

Over-the-air software and security updates shall be available; hardware upgrades are included in the plan. If the service provider changes network requirements, the connectivity and support plan include all software and hardware upgrades.

1/2/3/4/5-year connectivity and support plans shall be available.

- Software User Interface

The software user interface shall include a scrollable, zoom-able map display, with the SZB shown as a representative dynamic icon on the map. The map display must have the option of satellite view or standard street view. The map shall include the ability to see the SZB icons using Google Streetview.

The icons shall be able to identify if there is an alert status or if the SZB is offline.

The map display shall allow the operator to turn on layers which can display all SZB designations.  Operators shall also be able to overlay Google traffic information so they can see traffic together with the SZBs.

HTTP and HTTPS protocols and XML data structures for communications shall be utilized.

The software is cloud-based and shall meet NEMA TS 8 requirements for Cyber and Physical Security for Intelligent Transportation Systems.

The software shall display the alert/fault status, last communication with the device, real-time, minimum and maximum values for battery voltage, solar panel voltage, on/off status, door open/closed, or local manual override control. These parameters can be viewed in graphical form.

When a fault occurs, real-time alerts shall be published via SMS and/or email.  The alert will be immediately sent to the response personnel.

Key performance indicators shall be recorded by the software and reported on a weekly or daily basis. The report shall include details on the health condition of the batteries, solar panels and LED modules. The following types of reports shall be available: Alerts, User-Activity, SZB Operation, Fault Repair Response Time.

Alerts shall be displayed by color codes to indicate priority and critical nature of the alert.

Raw data, error logs, and communication logs shall be available for diagnostics.  The logs shall be print-ready or downloadable to spreadsheet.

SZB schedules, events, holidays, and program delays shall be set-up and downloaded remotely via the software.  The schedule shall be published to one or more SZBs simultaneously.

The software shall be capable of immediate manual override of individual or networks of SZBs in the event of early release or other unexpected school events.

Up to 20 unique schedules, unlimited holidays, exceptions, and overrides shall be available.

- Smartphone Mobile Safety App

The smartphone app shall be compatible with iOS and Android devices.

The smartphone application shall provide audible alerts to users. The application shall not require any user interaction and shall always run in the background.

Users shall be capable of receiving visual alerts via the smartphone application.

Users shall be capable of seeing speed limits for active school zones and receive warnings when speeding in an active school zone.

Users shall have the ability to turn on/off audible alarms for the various applications.

Users shall be capable selecting the form of transportation, such as pedestrian, cyclist, or motorist.

The smartphone application shall support the following applications as standard:

- SPaT/MAP display of signal timing – V2I

- Red-light running at traffic signals – V2I

- Emergency vehicle and bus priority – V2I

- Direction of approaching emergency vehicle – V2V

- Intelligent cross walks – V2I

- Intelligent school beacons – V2I

- Motorist to Cyclist and Pedestrians Warnings - V2V

- Rear end collision warning – V2V

- Virtual/advance traffic detectors at traffic signals – V2I

- Curve warning/reduce speed – V2I

- Wrong way detection – V2I

- Configuration

The SZB cabinet shall house an auto-scrolling LED on-board user interface that provides on-site configuration adjustment, system status and fault notification, built-in system test, and programming of optional internal calendar settings. The SZB shall have an optional USB interface for programming the internal calendar, and an optional pole-mounted programming junction box for housing the USB interface.

The user interface shall provide a display of four (4) alphanumeric characters and three (3) control buttons to navigate and change settings and activate functions.

When editing the configuration, the user interface will flash the display indicating it is ready to accept editing and will flash the display rapidly 3 times to indicate the setting change has been accepted.

The system shall provide configurable nighttime intensity settings ranging from 10% to 100% of daytime intensity.

The SZB shall be provided with an optional built-in internal calendar function that allows users to program multiple on/off sequences every day for at least one calendar year.  The calendar shall be programmed via USB connection made available to users within the solar engine.  An optional external weather-proof box and harnessing shall be made available for programming of the SZB from the base of the mounting structure.

The beacons will flash when activated either by an optional internal calendar within the controller or by contact closure provided by a third-party device.  Flashing will continue until either the internal calendar discontinues it or contact closure from the monitoring unit or a third-party device is removed.  Contact closure control by third-party devices shall be offered as “Normally Open” or “Normally Closed”.

The SZB shall be capable of enabling or disabling ambient brightness auto-adjustment.  This feature allows the system to provide optimal output brightness in relation to ambient light levels.  If enabled, the ambient brightness auto-adjustment shall adjust output to a range between 50% and 100% of daytime intensity.

The User Interface shall provide viewing and/or programming access for the following:

- Digital output that is active during the flashing cycle that allows the notification or control of external devices such as overhead illumination.  Digital output shall be configurable for night operation only or operation day or night

- 6 Flash Patterns

- Radio Channel (Choice of 1 to 14) if equipped

- Radio Status if equipped

- Calendar On/Off Control

- Calendar Master/Slave control of calendar broadcast via radio if equipped

- Night Intensity Setting

- Adjustment for Ambient Daytime Brightness

- Intensity (20 mA to 1400 mA)

- Self-Test / BIST (Built-In Self-Test) including the detection of shorts or open circuits in the fixture outputs

- Battery Status – General description and actual battery voltage

- Day or Night Status (as determined by dedicated photosensor not solar panel output)

- Solar Panel Voltage

- Automatic Light Control.  If this safety feature is enabled, it allows the SZB to temporarily reduce the intensity of the beacons to maintain energy equilibrium. The user interface shall report the amount of dimming being applied in the range of 10% to 100%

- Firmware Version number

On/off activation, night intensity setting and adjustment for ambient daytime brightness shall be automatically broadcast to all radio-equipped SZBs in the system when changed in one radio-equipped SZB.

- Operational Specifications

The SZB shall conform to all applicable provisions of the MUTCD and shall provide configurable intensity settings up to and including the ITE VTCSH LED circular signal supplement requirement.

The SZB shall offer an MUTCD-compliant flash pattern and activation including alternate, unison and quick-flash

The SZB shall conform to the provisions of the MUTCD 2009 Edition Chapter 4L. Flashing Beacons standard of a flash rate of not less than 50 or more than 60 times per minute, where the illuminated period of each flash shall be a minimum of 1/2 and a maximum of 2/3 of the total cycle.

The SZB shall use a dedicated light sensor to detect night and day states and apply any optionally enabled intensity adjustments.

The SZB, including the approved third-party time switch, shall have the capacity to operate at an agency-specified number of hours per day, and a specified number of days per week using the available solar radiation at the installation location.

- Radio System

The SZB shall have an optional 2.4GHz radio that allows one “Master” SZB equipped with internal or external calendar system to remotely command multiple “Slave” SZBs within range to turn ON or OFF in synchrony with the Master SZB.

The SZB shall have the capability to activate other SZBs by wireless communications within 1,000 feet (304 meters).

The SZB shall have a minimum of 14 unique channels that can be configured on-site to avoid inadvertent activation of nearby SZBs.

The antenna shall be a low-profile “button” shape that cannot be bent or broken by vandals

All SZBs in the system shall initiate activation simultaneously within 150ms of activation.

- Activations

The SZB shall be activated remotely by the factory-installed monitoring unit or activated locally via included operational mode switch.

With optional local wireless, all SZBs in a master/slave configuration shall initiate activation simultaneously within 150ms of activation.

- Environmental Testing

The SZB cabinet and beacons shall be rated to a minimum of NEMA 3R.

- Packaging

Packaging shall consist of only recyclable corrugated cardboard and soft plastic bags.

- Qualifications

The SZB shall be FCC certified to comply with all 47 CFR FCC Part 15 Subpart B Emission requirements.

The SZB shall be manufactured in the USA and shall be Buy American compliant.

Manufacturer shall provide a 5-Year Limited Warranty.  Battery warranty shall match the connectivity plan (ie. either 1/2/3/4/5-years).

The Manufacturer shall be ISO 9001 certified.

Manufacturer: Carmanah Technologies Inc.

Model: R829-G_AC School Zone Flashing Beacon with StreetHub

Toll-Free: 1-877-722-8877

www.carmanah.com