Purchase Specification

for a

AC-Powered Cabinet-Based Rectangular Rapid Flashing Beacon (RRFB) with Remote Connectivity

- Overview

Each RRFB shall have the capability to remotely connect to a cloud-based platform allowing for two-way communication and control. Each RRFB shall consist of a cabinet-based solar engine with one to four light bars using AC power.  The industry-standard cabinet will house the charge controller, flash controller, on-board user interface, wireless communications, battery and a monitoring unit which includes GPS and cellular modem with optional ethernet connection and RS-232 port.  The RRFB shall conform to all provisions of the MUTCD, Interim Approval IA-21 including flash pattern.  The RRFB shall be pre-wired to the maximum extent possible.  Solar-powered version of the RRFB shall also be available, including a smaller self-contained version that is fully compatible.

- Mechanical Specifications

The control cabinet shall be constructed from aluminum with a lockable industry standard #2 lock and tamper-proof hinged door.  No other external control cabinet shall be required. The control cabinet shall be vented to provide air circulation and cooling of the electronic system.  The vents shall be screened to prevent ingress by insects and debris.

The overall weight of the control cabinet shall not exceed 90lbs (41 kg) and shall have the approximate dimensions: 24” H x 16” W x 8” D (61cm H x 41cm W x 21 cm D).

Fasteners shall be stainless steel.

The internally mounted monitoring unit shall be a single piece of equipment and not required any peripheral attachments except for, the GSM and GPS antenna lead wires for the externally mounted antenna.

The externally mounted integrated GSM/GPS antenna shall be a suitable weather-resistant design and shall mount directly to the top surface of the control cabinet without the requirement for additional hardware.

The monitoring unit shall be capable of being programmed locally via a laptop interface and ethernet.

The monitoring unit shall be capable of receiving over-the-air software and security updates via cellular communication. Physical trips to the monitoring unit shall not be required for updates.

The monitoring unit shall be connected-vehicle ready and capable of communicating safety messages to motorists via cellular infrastructure and a smartphone app. The monitoring unit shall support the SAE J2735 standard for connected vehicle messages. The monitoring unit shall support both cellular and optional DSRC technology. The smartphone app is freely available to all users, including pedestrians, cyclists and motorists.

The monitoring unit shall be covered under warranty if the device is under an active connectivity and support plan and is connected to the RRFB.

- Fixtures

- Light bars

The light bars shall be current-driven LED strings without active electronics.  The LEDs shall be driven by pulse-width modulated fixed current.

The light bar housing shall be constructed from aluminum and shall have the approximate dimensions: 24” L x 1.5” D x 4.5” H (61.0 cm L x 3.8 cm D x 11.4 cm H).

Each light bar shall conform to all provisions of the MUTCD and FHWA requirements.

Each of the two modules in a light bar shall have 8 LEDs and shall be purpose-built by the manufacturer of the RRFB including the optics.  The optics shall be premium, UV-resistant polycarbonate.

Each end of a light bar shall include a side-emitting pedestrian confirmation light composed of a single LED.  Users shall have the option of using both confirmation lights for median applications, or covering one confirmation light with an included sticker for side-of-road applications.

The light bar shall be mounted to the post or pole using a separate bracket assembly to facilitate mounting two light bars back-to-back (bi-directional) and to allow the light bar(s) to rotate horizontally for aiming.

The light bar bracket shall be constructed from galvanized or stainless steel and shall have both banding and bolting mounting options and shall be able to be mounted to all specified pole types.

The light bar assembly shall open for access to the wiring connections for the LED modules.  LED modules shall be rated to NEMA 3R.

Light bar wiring harnesses shall be included.

Fasteners shall be stainless steel.

- LED Enhanced Signs

The LED enhanced sign shall be available in 24, 30, 36, or 48” and typical MUTCD crossing warning signs such as the W11-2 (Pedestrian), W11-15 (Trail) and S1-1 (School) as applicable in MUTCD Chapter 2C and Chapter 7B respectively.  The sign sheeting shall be yellow or fluorescent yellow green (FYG) 3M Diamond Grade DG3 retroreflective with 3M anti-graffiti and overlay film or High Intensity Prismatic sheeting.

The LED enhanced sign shall consist of 8 yellow high-power LEDs in waterproof, polycarbonate impact-resistant housings that can be driven at a high intensity. Each housing shall be IP68 rated and tested for shock and vibration.

The LED optics shall be integrated total internal reflection (TIR) for optimal light efficiency and shall be premium, UV-resistant polycarbonate.  The optics shall be purpose-built by the manufacturer for optimal intensity.

In the event a single LED fails, all other LEDs shall continue to operate.

The LEDs shall be current-driven strings without active electronics.  The LEDs shall be driven by pulse-width modulated fixed current.

The LED bezel shall be black and placed within the border of the sign for enhanced LED contrast and increased visibility.

The LED wiring shall be covered by aluminum channels. There shall be no gaps or exposed wiring between the channels and LED modules or from the sign to the pole. All harnessing must be concealed and vandal resistant.

- Mounting

Mounting adapter hardware for the RRFB cabinet shall accommodate 4” – 4.5” round poles or square posts.

The solar panel shall be available in the following configurations:

4.5” Diameter Round Top-of-Pole Mount

4.5” Diameter Round Top-of-Pole Heavy Duty Mount

4” – 4.5” Side-of-Pole Mount

Side-of-Pole mounting shall offer strapping as standard with an option for Z-bar and U-bolts.

Mounting configurations shall not require specialized tools.

- Connectivity and Support Plan

The RRFB shall include cloud hosted software with user web-based access.  Other software or IT infrastructure shall not be required for installation or maintenance.

The user interface shall be web based and viewable using a browser, either Chrome, Internet Explorer, or Firefox, as well as Safari on an iPad.

Cellular communication shall use the latest 3G, 4G and LTE and LTE wireless broadband networks.

The cloud software shall be mobile friendly and operate without requiring a static IP address.  Operators shall be able to access the data on a mobile phone.

Over-the-air software and security updates shall be available, and hardware shall be upgradeable if the service provider changes network requirements.

The user interface shall include a scrollable, zoom-able map display, with the RRFB shown as a representative icon on the map. The map display must have the option of satellite view or standard street view. The map shall include the ability to see the RRFB icons using Google Streetview.

The icons shall be able to identify if there is an alert status or if the RRFB is offline.

The map display shall allow the operator to turn on layers which can display all RRFB designations.  Operators shall also be able to Google traffic overlay information so they can see traffic together with the RRFBs.

An integrated GPS shall allow RRFB geolocation.

If cell service is interrupted or unavailable, events shall be stored in internal memory, and automatically forwarded when cell service is restored.  Battery back-up shall also be available for continual operation.

The field controller shall autonomously ping every 30 minutes to ensure online connectivity.

HTTP and HTTPS protocols and XML data structures for communications shall be utilized.

The cloud software shall meet NEMA TS 8 requirements for Cyber and Physical Security for Intelligent Transportation Systems.

The user interface shall display the alert/fault status, last communication with the device, real-time, minimum and maximum values for battery voltage, solar panel voltage, on/off status, or door open/closed. These parameters can be viewed in graphical form.

When a fault occurs, real-time alerts shall be published via SMS and/or email.  The alert will be immediately sent to the response personnel.

Key performance indicators shall be recorded by the software and reported on a weekly or daily basis. The report shall include details on the health condition of the batteries, solar panels and LED modules. The following types of reports shall be available: Alerts, User-Activity, RRFB Operation, and Fault Repair Response Time.

Alerts shall be displayed by color codes to indicate priority and critical nature of the alert.

Raw data, error logs, and communication logs shall be available for diagnostics.  The logs shall be print-ready or downloadable to Excel.

The interface shall show current, min, max and average system activations as recorded within 15-minute intervals over a 24-hour period. A monthly summary of activations shall be available and viewable in graphical form.

1/2/3/4/5-year connectivity and support plans shall be available.

- Smartphone App

The smartphone application shall provide audible alerts to users. The application shall not require any user interaction and shall always run in the background.

Users shall be capable of receiving visual alerts via the smartphone application.

Users shall be capable of seeing speed limits for active school zones and receive warnings when speeding in an active school zone.

Users shall have the ability to turn on/off audible alarms for the various applications.

Users shall be capable selecting the form of transportation, such as pedestrian, cyclist, or motorist.

The smart phone application shall support the following applications as standard:

- SPaT/MAP display of signal timing – V2I

- Red-light running at traffic signals – V2I

- Emergency vehicle and bus priority – V2I

- Direction of approaching emergency vehicle – V2V

- Intelligent cross walks – V2I

- Intelligent school beacons – V2I

- Motorist to Cyclist and Pedestrians Warnings - V2V

- Rear end collision warning – V2V

- Virtual/advance traffic detectors at traffic signals – V2I

- Curve warning/reduce speed – V2I

- Wrong way detection – V2I

- Configuration

The RRFB cabinet shall house an auto-scrolling LED on-board user interface that provides on-site configuration adjustment, system status and fault notification.

The user interface shall provide a display of four (4) alphanumeric characters and three (3) control buttons to navigate and change settings and activate functions.

When editing the configuration, the user interface will flash the display indicating it is ready to accept editing and will flash the display rapidly 3 times to indicate the setting change has been accepted.

The flash duration shall be adjustable in-the-field from 5 to 60 seconds in one second increments, 60 to 1,200 seconds in 60-second steps, and 3,600 seconds.  Default flash duration shall be 20 seconds.

The system shall provide configurable nighttime intensity settings ranging from 10% to 100% of daytime intensity.

The system shall be capable of enabling or disabling ambient brightness auto-adjustment.  This feature allows the system to provide optimal output brightness in relation to ambient light levels while always maintaining adherence to SAE J595 Class I specifications.  If enabled, the ambient brightness auto-adjustment shall adjust output to a range between 50% and 100% of daytime intensity.

The User Interface shall provide viewing and/or programming access for the following:

- Activation Duration (5 to 60, 60 to 1200, or 3600 seconds)

- Digital output that is active during the flashing cycle that allows the control of external devices such as crosswalk illumination.  Digital output shall be configurable for night operation only or operation day or night

- Radio Channel (Choice of 1 to 14)

- Radio Status

- Night Intensity Setting

- Adjustment for Ambient Daytime Brightness

- Self-Test / BIST (Built-In Self-Test) including the detection of shorts or open circuits in the fixture outputs

- Battery Status – General description and actual battery voltage (not applicable for AC model)

- Day or Night Status (as determined by dedicated photosensor)

- Solar Panel Voltage (not applicable for AC model)

- Automatic Light Control.  If this safety feature is enabled, it allows the RRFB to temporarily reduce the intensity of the light bars to maintain energy equilibrium.  The user interface shall report the amount of dimming being applied in the range of 10% to 100%

- Daily activations averaged over 90 days

- Pushbutton detection

- Firmware Version number

Activation duration, Night intensity setting and adjustment for ambient daytime brightness shall be automatically broadcast to all RRFBs in the system when changed in one RRFB.

- AC/DC Power Supply

The RRFB shall include a universal AC/DC power supply that accepts conventional AC power input and outputs 15 volts DC.  It shall be rated for at least 50 watts.  AC wiring input shall terminate on a DIN-rail circuit breaker rated for 4 amps.

- Operational Specifications

The RRFB shall meet the minimum photometric specifications of the Society of Automotive Engineers (SAE) standard J595 Class I dated January 2005.  A photometric report by a certified third-party testing laboratory shall be provided to demonstrate compliance with J595.

The color of the yellow light bar indications shall meet the specifications of SAE standard J578 (Color Specification) dated December 2006.

The controller shall be able to support up to 1.4 amps combined current through the RRFB fixtures simultaneously.

The system shall use a dedicated light sensor to detect night and day states and apply any optionally-enabled intensity adjustments.

The system shall operate normally within the temperature range of -40 to +161˚F (-40 to +72˚C)

- Radio System

The radio system shall operate at 2.4GHz

Upon detection of a pushbutton press, an RRFB will broadcast an activation to all other nearby RRFBs sharing the same channel.

The RRFB shall have the capability to activate other RRFBs by wireless communications within 1,000 feet (304 meters).

The RRFB shall have a minimum of 14 unique channels that can be configured on-site to avoid inadvertent activation of nearby systems.

The antenna shall be a low-profile “button” shape that cannot be bent or broken by vandals

- Activations

The system shall be capable of activation by either pedestrian push button, pedestrian push button with voice message, or passive detection. The RRFB shall be capable of operating with either 1 or 2 pushbuttons.

The pedestrian push buttons shall have an LED indicator with audible tone with Piezo control and shall be ADA compliant. The pedestrian push button with voice message shall have three LED indicators, locate tone, and voice message with the MUTCD IA-21 approved message “Yellow lights are flashing”.  The message shall be spoken twice. The push button shall be ADA compliant with directional arrow. A solar simulation shall be provided to verify the push button with voice message load can be supported by the RRFB for reliable year-round operation.

The passive detection system shall use a short-range microwave sensor providing the necessary range at a low power consumption.  The passive detection system shall provide pedestrian presence detection within the targeted area of a crosswalk or trail crossing. A solar simulation shall be provided to verify the microwave sensor load can be supported by the RRFB for reliable year-round operation.

All RRFBs in the system shall initiate activation simultaneously within 150ms of activation.

If an additional activation occurs while the system is activated, the flash duration shall reset.  For

example, with the flash duration set to 20 seconds, if an additional activation occurs after the RRFB has been activated for 15 seconds the RRFB will continue for an additional 20 seconds, or 35 seconds in total.

If the RRFB has ceased operation, any subsequent activation shall activate the RRFB without delay regardless of how recently the RRFB ceased operation.

Pushbutton wiring harnesses shall be included.

- Environmental Testing

The RRFB cabinet and light bars shall be rated to a minimum of NEMA 3R.

- Packaging

Packaging shall consist of only recyclable corrugated cardboard and soft plastic bags.

- Qualifications

The RRFB shall be FCC certified to comply with all 47 CFR FCC Part 15 Subpart B Emission requirements.

The RRFB shall be manufactured in the USA and shall be Buy American compliant.

Manufacturer shall provide a 5-Year Limited Warranty.  Battery warranty shall match the connectivity plan (ie. either 1/2/3/4/5-years).

The Manufacturer shall be ISO 9001 certified.

Manufacturer: Carmanah Technologies Inc.

Model: SC315-G_AC RRFB with StreetHub

Toll-Free: 1-877-722-8877

www.carmanah.com